Download and install raspbian (jessie)

scan for ip on your network to find newly booted rpi
nmap -sn 192.168.0.0/24 and ssh to rpi
run raspi-config
enable SPI – will be needed by the display

do not forget to:
sudo apt-get update
sudo apt-get upgrade

Change default name of the server from raspberry to any thing you want by modifying the file /etc/hostname
/etc/hosts

and run:
sudo /etc/init.d/hostname.sh

Change dhcp to fixed ip (or do this on your router, servers should have fixed ip:
in file /etc/dhcpcd.conf at the bottom add:

interface eth0
static ip_address=192.168.0.10/24
static routers=192.168.0.1
static domain_name_servers=192.168.0.1
interface wlan0
static ip_address=192.168.0.11/24
static routers=192.168.0.1
static domain_name_servers=192.168.0.1

Make the network settings coresponding to your home network

“install” if desired a passwordless ssh (it accelerate the work)
https://www.raspberrypi.org/documentation/remote-access/ssh/passwordless.md

Install display SainSmart 1.8" TFT Farb LCD

https://github.com/notro/fbtft/wiki#install

Add to file /etc/modules-load.d/fbtft.conf
spi-bcm2835
fbtft_device

Add to file /etc/modprobe.d/fbtft.conf
options fbtft_device name=sainsmart18 rotate=270

Consider the rotate parameter according to your own hardware setup or think twice before you glue it.

It is always good to see, on a headless device some booting or shutdown messages. As we have now a LCD head, let's enable it as a console device:
To use the display as a console, add this to the end of the line in /boot/cmdline.txt
fbcon=map:10

Make the console font smaller
sudo apt-get install kbd

sudo dpkg-reconfigure console-setup

Encoding to use on the console: <UTF-8>
Character set to support: <Guess optimal character set>
Font for the console: Terminus (default is VGA)
Font size: 6x12 (framebuffer only)

Switch off Console blanking
This is set in /etc/kbd/config:
BLANK_TIME=0
and to the /etc/rc.local
setterm --blank 0

and add to the file /etc/modules
i2c-dev
spi_bcm2708
fbtft
fbtft_device name=sainsmart18 rotate=270 verbose=0

Prepare power pin for usb dvb tuner – at boot time we need “1” to enable modules loading
https://www.raspberrypi.org/documentation/configuration/pin-configuration.md

GPIO initialization at the boot time for power relay steering done via GPIO 1 (BCM GPIO 18) requires changing the default settings described in the blob file /boot/dt-blob.bin. Get the compiler

sudo apt-get install device-tree-compiler

Download the file dt-blob.dts for example from the above link, look at the bottom of the article:
https://www.raspberrypi.org/documentation/configuration/images/dt-blob.dts
or the better way is to create your won *.dts file out of your current hardware installation by:
on RPI in the local directory ~/dts call:
dtc -I dtb -O dts -o dt-blob.dts /boot/dt-blob.bin

 In the file dt-blob.dts depending on your hardware revision modify section of
pins_2b1 { // Pi 2 Model B rev 1.0
for the entry of pin@p18 (GPIO 1) such as:
pin@p18 { function = "output"; termination = "pull_down"; drive_strength_mA = < 8 >; startup_state = "active"; }; // My relay active at start

I added this also for the definition of pins_2b2 { // Pi 2 Model B rev 1.1
Eventually compile ZZ compile the new blob file:
sudo dtc -I dtb -O dts -o dt-blob.dts /boot/dt-blob.bin

Install DVBSky S960 USB tuner
Check the link https://www.linuxtv.org/wiki/index.php/DVBSKY_S960 for details
S960 is supported out of te box by RPI on Jessie, we need only to download firmware file from:
http://www.dvbsky.net/Support_linux.html
extract all files to local folder
dvb-fe-ds3103.fw
dvb-demod-m88ds3103.fw
dvb-demod-m88ds3103.fw
and move all of them to /lib/firmware/
sudo mv *.fw /lib/firmware

1. Install tvheadend
  sudo apt-get install apt-transport-https
  compile or instal from repo – here how to with repo:
  https://tvheadend.org/projects/tvheadend/wiki/AptRepository
  First install bintray's GPG key:
  sudo apt-key adv --keyserver hkp://keyserver.ubuntu.com:80 --recv-keys 379CE192D401AB61
  echo "deb https://dl.bintray.com/tvheadend/deb jessie release" | sudo tee -a /etc/apt/sources.list
  where
  This is for “jessie” Raspian version. In the tvheadend official repo there is only a “release” version no unstable or stable options.
  Install tvheadend
  sudo apt-get install tvheadend
  Disable tvheadend service at the boot time – we start it only if necessary via local menu or via web in order to save energy when not used
  sudo update-rc.d -f tvheadend remove

Tvheadend configuration requires several steps – google for it. It aso takes time to scan all multiplexers – be patient.

Install oscam server
Download the oscam binary file from http://download.oscam.cc/index.php?direction=1&order=mod&directory=1.20_TRUNK/Raspberry
Extract oscam binary file and copy it to /usr/local/bin
Check the permision:
sudo chown root:root /usr/local/bin/oscam
sudo chmod 755 /usr/local/bin/oscam

Modify all necessary files according to your pay-tv provider. I'm not providing any help on this and I'd like to remind that watching pay-tv without required contract is illegal (at least in most of the countries). Eventually copy the files to /usr/local/etc

You have to configure the oscam server, which is independent from pay-tv. For the Easymouse 2 USB Smart Card reader, which I used in my project following settings are fine:
protocol = mouse
device = /dev/ttyUSB0
detect = dc

Jessie is ready to provide all USB libraries, just setup your Easymouse 2 USB Smart Card according to your card requirements plug and check if it is visible (lsusb).
Create oscam startup script in /etc/init.d folder
I use following file as an oscam startscript

#! /bin/sh
### BEGIN INIT INFO
# Provides: Oscam
# Required-Start: $remote_fs $syslog
# Required-Stop: $remote_fs $syslog
# Default-Start: 2 3 4 5
# Default-Stop: 0 1 6
# Short-Description: Oscam init script
# Description: Launch oscam at startup
### END INIT INFO

DAEMON=/usr/local/bin/oscam
DEAMON_OPTS="-b -r 2 -c /usr/local/etc"
PIDFILE=/var/run/oscam.pid

test -x ${DAEMON} || exit 0

. /lib/lsb/init-functions

case "$1" in
    start)
log_daemon_msg "Starting OScam"
start-stop-daemon --start --quiet --background --pidfile ${PIDFILE} --make-pidfile --exec ${DAEMON} -- ${DAEMON_OPTS}
log_end_msg $?
    ;;
    stop)
log_daemon_msg "Stopping OScam"
start-stop-daemon --stop --exec ${DAEMON}
log_end_msg $?
        sleep 10
    ;;
    force-reload|restart)
    $0 stop
    $0 start
    ;;
  *)
    echo "Usage: /etc/init.d/oscam {start|stop|restart|force-reload}"
    exit 1
    ;;
esac

exit 0

and here we add this service to the default startup procedure (as this does not consume too much energy)
sudo update-rc.d oscam defaults

Install required python libraries

- transitions, a lightweight, object-oriented finite state machine implementation in Python
- psutil
- gevent

sudo apt-get install build-essential python-dev python-pip
sudo pip install transitions
sudo pip instal psutil
sudo pip instal gevent

Install python software to manage services on RPI including graphic interface, rotary knob and web
Create graphical menu with rotary knob:
git clone https://github.com/petervflocke/rotaryencoder_rpi menu
Create web interface
git clone https://github.com/petervflocke/flasksse_rpi web

Start both programs after the boot, add some log cleaning
sleep 3
gpio mode 1 output
gpio write 1 0
python /home/pi/menu/main.py&
python /home/pi/web/sse.py&
Explanation:
gpio action – the tuner starts always with power on – it secures loading respective modules etc. If it is not used (no dvb streaming) it satys plug in into usb but the 12V power supply can be switched off to decrease energy consumption. It works fine with the DVB S960 USB Tuner
finaly starts two programs one for display and rotary knob and the other for web interface. I want to have both to be able quickly access system menu.

Housekeeping
Disable swaping:
sudo dphys-swapfile swapoff
consider of moving log files to ramdrive and or read on clean logs, which consumes space on sd drive.